## Slide 1: Coastal Navigation
Piloting in the Modern World
tdgil.com

## Slide 3: Agenda
Friday
  Tools, Resources, and Navigation Aids
  Tides and Currents
  Latitude and Longitude
Saturday
  Dead Reckoning
  Piloting
Sunday
  Piloting Practice
  Test

## Slide 4: Tools, Resources, and Navigation Aids

## Slide 5: Navigation Tools

## Slide 6: Essential Tools
Plotting Tools
  Dividers/Compass
  Parallel rule
  Roller plotter
  Triangles
Miscellaneous
  Pencils
  Erasers
  Calculator
  Watch

## Slide 7: Plotting Tool Examples

## Slide 8: Essential Tools
Compasses
  Ships Compass
  Handheld Compasses
Navigation Logbook
Plotting Sheets
  Universal Plotting Sheet
  Maneuvering Board

## Slide 9: Publications
Charts
  NOAA Charts
    Print on demand
    Raster Charts (look like paper charts)
    Electronic Navigation Charts (ENC) - Vector Charts
  Chart No. 1 (not really a chart)
Publications
  Coast Pilot
  Sailing Directions Enroute
  Notice to Mariners
  Local Notices to Mariners
  Light List
  List of Lights
  American Practical Navigator
Office of Coast Survey (NOAA) – https://nauticalcharts.noaa.gov/
USCG NAVIGATION CENTER – https://www.navcen.uscg.gov/
National Geospatial Agency – https://msi.nga.mil/

## Slide 10: Which to Use When?
Local Notices to Mariners (LNM) vs. Notice to Mariners?
  LNM is the best source to update charts and identify hazards in a specific sailing area
  The Notice to Mariners covers the entire U.S.
    A great starting point if approaching U.S. waters from International Waters.
    May not have as much detail as the LNM
Light List vs. List of Lights?
  Light List identifies aids to navigation in U.S. waters.
  List of Lights identifies aids in other countries.
Coast Pilot vs. Sailing Directions Enroute?
  Coast Pilot is uses for U.S. waters
  Sailing Directions Enroute is used for navigation to and in other countries.

## Slide 11: Navigation “Must Have” Publications
Chart(s) of Your Sailing Area
  When sailing in the ocean near San Francisco, I ALWAYS have 4 charts
    Entrance to San Francisco Bay (18649), Gulf of the Farallones (18645), Drakes Bay (18647), and Half Moon Bay (18682)
Chart No. 1 (this is a book, not a chart). It is OK to have it downloaded as a PDF file.
Coast Pilot (No. 7 around here) – I like to download it and print off applicable pages for study and notes.
Light List – downloaded.
Local Notices to Mariners – download it Thursday; STUDY IT!
Bonus “Must Have” – US Aids to Navigation System – Printed and waterproof

## Slide 12: ATONs (Aids to Navigation)
Lateral Aids
Safe Water Marks
Regulatory Marks
Danger Marks
Definition
mark, n. 1. An artificial or natural object of easily recognizable shape or color, or both, situated in such a position that it may be identified on a chart. A fixed artificial navigation mark is often called a BEACON. This may be lighted or unlighted.

## Slide 13: Tides and Currents

## Slide 14: Finding Tide and Current Projections
NOAA Tide and Current Homepage
  https://tidesandcurrents.noaa.gov/
Tides
  https://tidesandcurrents.noaa.gov/tide_predictions.html
Currents
  https://tidesandcurrents.noaa.gov/noaacurrents/Regions

## Slide 15: Currents

## Slide 16: NOAA Currents Website
NOAA Currents – https://tidesandcurrents.noaa.gov/noaacurrents/Regions

## Slide 17: Advanced Coastal Cruising August 26-29, 2021

## Slide 19: Tides

## Slide 20: 2020 Modern “Tide book”
https://tidesandcurrents.noaa.gov/tide_predictions.html

## Slide 23: Rule of twelfths
First hour 1/12th
Second hour … another … 2/12th
Third hour … another … 3/12th
Fourth hour … another … 3/12th
Fifth hour … another … 2/12th
Sixth hour … another … 1/12th
Example … low tide of zero, high of 6’
1/12th of 6’ equals .5’
1 hour after low, tide would be .5’
2 hours after low, tide would be 1.5’ (.5 plus 1)
3 hours after low, tide 3’ (1.5 plus 1.5)

## Slide 24
You plan to moor at Angel Island on Valentines Day. The depth of the mooring field is 4.5 feet at a zero tide. Your boat draws 6.5 feet.
What is the latest time (to the whole hour before) on Sunday you will have sufficient water to reach your mooring ball?
What time after 8:00AM Monday will you have enough water to leave the mooring field?

## Slide 25
You plan to moor at Angel Island on Valentines Day. The depth of the mooring field is 4.5 feet at a zero tide. Your boat draws 6.5 feet.
5.1H - 0.21L = 4.89 tidal change / 12 = .4
5.1 – .4 = 4.7
1507 4.7 – .8 = 3.9
1607 3.9 – 1.2 = 2.7 Last chance to moor is 1600
1707 2.7 – 1.2 = 1.5
1807 1.5 – .8 = 0.7
1907 0.0 – .4 = 0.3
0800 4.6H - 1.8L = 2.8 tidal change / 12 = .2
0900 1.8 + .2 = 2.0
1000 2.0 + .4 = 2.4 May as well sleep in

## Slide 26: Latitude and Longitude

## Slide 27: Projections
Prime Meridian
Mercator Projection
Equator
West
East
East
North
South

## Slide 29: Practice Exercises – Finding Given Lat & Lon
Using the Gulf of the Farallones Chart excerpt
  What is the name of the object at 37 51.6’ N; 122 41.6W
  What is the name of the object at 38 00.3’ N; 122 58.0W
  What is found at 37 56.7’ N; 122 53.2W

## Slide 30: Practice Exercises – Finding Given Lat & Lon
Using the Gulf of the Farallones Chart excerpt
  What is the name of the object at 37 51.6’ N; 122 41.6W
    G ”1DR” Fl G 6s
  What is the name of the object at 38 00.3’ N; 122 58.0W
    “CG”
  What is found at 37 56.7’ N; 122 53.2W
    Center of the compass rose

## Slide 32: Practice Exercises – Finding Lat & Lon
Using the Coast Outline Chart Locate the Following Lat & Lon Locations
  37 50.6’ N; 122 35.5W (Label ”A”)
  37 52.1’ N; 122 52.5W (Label ”B”)
  38 03.3’ N; 122 46.4W (Label ”C”)

## Slide 33
A
B
C

## Slide 34: Distance Speed and Time

## Slide 35: Practice Exercises – Finding Direction & Distance
Using the Coast Outline Chart Positions Just Plotted
  What is the distance from Point A to Point B
  What is the course from Point A to Point B
  What is the distance from Point B to Point C
  What is the course from Point B to Point C
  What is the distance from Point C to Point A
  What is the course from Point C to Point A

## Slide 36: Practice Exercises – Finding Direction & Distance
Using the Coast Outline Chart Positions Just Plotted
  What is the distance from Point A to Point B
  What is the course from Point A to Point B
  What is the distance from Point B to Point C
  What is the course from Point B to Point C
  What is the distance from Point C to Point A
  What is the course from Point C to Point A
  13.5nm
  277T
  12.2nm
  023T
  15.3nm
  146T

## Slide 37
A
B
C
C 277
D 13.5
C 023
D 12.2
C 146
D 15.3

## Slide 38: Intro to Distance/Speed/Time Equations
⚓️ Distance/Speed = Time
⚓️ Distance/Time = Speed
⚓️ Speed X Time = Distance
6-Minute Rule - Distance traveled in 6 minutes multiplied by 10 = speed
6-Minute Rule #2 – 6 minutes is .1 hours … 12 minutes is .2 hours … etc.

## Slide 39: Practice Exercises – Determining Speed and Time
Using the Coast Outline Chart Courses and Distances Just Plotted (round to nearest tenth hour)
  At 4 knots how long to travel from A to B
  At 5.5 knots how long to travel from B to C
  At 6 knots how long to travel from C to A

## Slide 40: Practice Exercises – Determining Speed and Time
Using the Coast Outline Chart Courses and Distances Just Plotted (round to nearest tenth hour)
  At 4 knots how long to travel from A to B
  At 5.5 knots how long to travel from B to C
  At 6 knots how long to travel from C to A
  3.4 hours (3:24)
  2.2 hours (2:12)
  2.5 hours (2:30)

## Slide 41: Adding and Subtracting Time
Always Use 24 Hour Time Notation (10:52PM is 2252)
Leaving Point A at 0852 at 4 knots what is the ETA at Point B?
You Arrive At Point B at 1205 What was your actual speed?
Continuing to Point C at 5.5 knots what is your ETA?
The next morning, leaving Point C at 0950 at 6 knots, what is your ETA back at Point A?

## Slide 42: Adding and Subtracting Time
Always Use 24 Hour Time Notation (10:52PM is 2252)
Leaving Point A at 0852 at 4 knots what is the ETA at Point B?
08 52
03 24
11 76
+1 - 60
12 16
You Arrive At Point A at 1205 What was your actual speed?
12 05
-08 52
3 13 = 3.2 hours
13.5nm/3.2 = 4.2kts
Continuing to Point C at 5.5 knots what is your ETA? 1417
ETA at Point A is 12:20

## Slide 43: Piloting

## Slide 44: Dead Reckoning (DR)
Departure
Distance, Speed, and Time
Course vs Heading
Labels
⚓️ Distance/Speed = Time
⚓️ Distance/Time = Speed
⚓️ Speed X Time = Distance
6-Minute Rule - Distance traveled in 6 minutes multiplied by 10 equals speed
The only factors to be used in a DR plot are Course, Speed, and Time

## Slide 45: Dead Reckoning (DR)
Basic Labels
Course (C) on Top of Line Always in True
Speed (S) and/or Distance (D) Below Line
Time of Fixes Written Horizontally
DR Times Written Diagonally
Dot with Circle = Fix
Dot with Square = Estimated Position
Dot with Partial Circle = DR Position

## Slide 46: Piloting
Lines of Position (LOP)
  Bearing to an object
  Line of Position by Range
  Depth Contour
Distance Off
  Angle off the bow
  Doubled Angle Fix
Fix
Running Fix
Estimated Position
Danger Bearings
  Constant bearing decreasing distance
  NMT/NLT
Piloting Definition: Navigation involving frequent or continuous determination of position relative to observed geographical points, to a high order of accuracy; directing the movements of a vessel near a coast by means of terrestrial reference points.

## Slide 47: LOP by Bearing to an object
B 067
B 115
Bearing to Pt Montara Light
  067 True (053 Magnetic)
Bearing to Pillar Point Radar Dome
  115 True (101 Magnetic)
Two LOPs provide a two-bearing fix

## Slide 48: LOP by Range
A ”Range” is two objects in line
Point Campbell on Angel Island when lined up with Peninsula Point on Belvedere provides a line of Position by Range

## Slide 49: LOP by Depth Contour
The 20 Fathom contour running southeast from Drakes Bay makes a good LOP
Add a bearing to Double Point and you have a fix
B 090

## Slide 50: LOP by Distance Off (Double the Angle)
Distance traveled from A to B is equal to the distance from B to the object, providing a circle of position
Add in the bearing to the object at position B and you have a fix
045 R
090 R
A
B
Two bearings of same object where second bearing is double the angle on the bow of the first represents distance off at time of second bearing

## Slide 51: LOP by Distance Off (Radar Range)
Using the variable range marker (VRM) on a radar establishes a line of position around that object
Two radar ranges obtains two possible locations. Your DR or a third range provides a fix
One radar range plus any other lop provides a fix
2.5 nm
A
B
3.25 nm

## Slide 52: Running Fix (advancing a bearing)
A running fix is based on your DR plot
At 0938 a bearing is taken of the rock off the southern point of Double Point. The bearing is 100T
22 minutes later, at 1000, you have travelled 2.2 nm based on 6 kts, and plotted a new DR position.
Move (aka, advance) the 100T bearing line the distance traveled from 0938 to 1000. (Red line)

## Slide 53: Running Fix (Same Target)
Once you have advanced your first bearing (lop)
Take and plot a second bearing to the same target. In this case, 048T
Your fix is the intersection of the new bearing and the advanced bearing

## Slide 54: Running Fix (different target)
Running fix works with separate targets
Once you have advanced your first bearing (LOP)
Take and plot a second bearing to any other target. In this case 031T to Duxbury Point
Your fix is the intersection of the advanced LOP and the LOP to the new target

## Slide 55: Estimated Position
An estimated position uses a DR plot plus one LOP
Draw a line perpendicular to the LOP that runs through the DR position
The estimated position is the point the LOP and the perpendicular line intersect
Estimated Position is not a fix. Do not reset the DR Plot

## Slide 56: Danger bearing
NMT 091M
B 099M
Red line represents danger bearing drawn to the buoy to keep clear of the rocks
A bearing of the buoy should never read more(or less) than set danger bearing (NMT 091m)
Bearing to buoy of 099m puts you in the danger area
Why magnetic bearings?

## Slide 57: Effects of Wind, Currents and Tides
Leeway
Set
Drift
Tides
Tidal Currents

## Slide 58: Estimating Leeway
360 
200
160
180
360 
190
150 
170 
Must be measured with no current present
If the center of your wake is the reciprocal of your heading, you have no leeway
Your wake should be approximately 39  from side to side (40  is close enough)
Find the reciprocal of your heading. In the examples that is 180 
Take a bearing down one leg of your wake. If you use the starboard wake, add 20  to get the center of your wake. If you use the port wake, subtract 20 
The difference between the reciprocal of your heading, and the centerline of your wake is your leeway.
In the left example, leeway is zero. In the right example, leeway is 10  to port. Your CMG in this case is 350 

## Slide 59: Finding Set and drift

## Slide 60: Course to steer

## Slide 62
BW “SR” Mo(A) WHISTLE @ 41 26.4’N; 71 13.5’W
W Or “C” BELL @ 41° 19.7’N; 071° 24’W
You depart “SR” at 0915. Boat Speed 5 kts
Distance to “C”?
ETA at “C”
Course True and Magnetic?
Relative Bearing of Point Judith Light upon arrival at “C”

## Slide 63
Continuing on the same course, at 1215, Block Island Southeast Light bears 224M and Point Judith Light bears 001M
What is your location?
Lat?
Lon?
What is your speed over ground.
What is the Set and Drift (hint: even though you have a fix, you need to find your DR position.

## Slide 64
From G “1B1” Fl G 4 sec BELL @ 41 15.5’N; 71 34.5’ Plot a course of 050T.
Depart “1B1” at 1300 @ 5kts
At 1400 Point Judith Light bears 022M
At 1440 Point Judith Light bears 311M
Complete a running fix
What is your location?
Lat?
Lon?

## Slide 65
At 0800, while underway at 5 kts, you are able to fix your location @ 41° 10.9 N; 071° 25.9’ W.
Plot a course to BW “WH” Mo (A) BELL @ 41° 29.4 N ; 071° 04.2 W
What is your course in True?
What is your ETA at WH?
At 0900 Point Judith Light bears 332M. Plot the bearing.
At 1000 Point Judith Light bears 293M.
What is your running fix location? Lat? Lon?
What is your CMG?
What is your SMG?
What is your Set?
What is your Drift?

## Slide 66
What is your new course to WH?
What is your course in True to steer to compensate for set and drift?
What is your course to steer in magnetic?
What is your course to steer per ships compass (include deviation)?
What is your new ETA at WH?
According to LNM, the GR mark at Elisha Ledge (41° 26.7’ N; 071° 09.5’ W) is missing. Set up at danger bearing to leave Elisha Ledge to port using the tank at Acoaxel (41° 30.5’ N; 071° 05.7’ W) as your target.
What is the danger bearing?